| Radio Shack HTX-202 2 Meter FM Transceiver |
| --- |
| Storing a frequency in memory |
| 1. Select VFO Mode | Press [VF] |
| 2. Enter Frequency | Enter the last 4 digits of the frequency. For instance, for 147.570, enter 7570. On a mistake, re-enter the digits. |
| 3. Select Tone Freq | Press [F] [M-SET] Press (SC or (SC to step up or down through the menus. At tc, rotate the tuning knob to select the Transmit Subaudible Tone. Press PTT to exit the menu and save the configuration. |
| 4. Turn on Tone Freq | Press [F] [T-SQL]. Confirm the T-SQL symbol is on |
| 5. Set the Offset | Press [F] [+/-] to toggle between +, -, or no offset. |
| 6. Store in Mem Channel | Press [F] and rotate the tuning knob to select the memory channel for writing. Press and hold [F] [M-WR] for 1 second to store the frequency into the selected channel. |
| 7. Select Memory Mode | Press [MR] |
| Other Operations |  |
| Clear Mem Channel | Press [MR] and select the memory channel to clear. Press [F] [M-CLR] to clear |
| Copy Mem to VFO | Press [MR] Select the channel, then press [F] [M-CLR] Press [VF] |

| Other Operations |  |
| --- | --- |
| Set Power | Press the Low Power button on top of the radio; IN for Low power, OUT for High Power. |
| Lock the Keyboard | Press [F] [LOCK]. The Lock symbol appears. Repeat to unlock. |
| Power Save | Press [F] [SAVE]. The Save symbol appears. Repeat to unlock. |
| Memory Scan | Press [MR] Press and hold (SC or (SC to scan in that direction. |
| Frequency Scan | Press [VF] Press [F] [M-SET] Press (SC or (SC to set the Scan limits. Press PTT to exit the menu and save the configuration. Press and hold (SC or (SC to scan in that direction. |
| Configuration Menu | Code Default Explanation oS 0.600 Duplex separation tc 88.5 Xmit Subaudible rc 88.5 Recv subaudible Sr 20 Frequency Step Sc ti Scan resume Sd 2.0 San Delay Time | S1 144.00 Low scan range S2 148.00 High scan range Ud dn Vacant scan dir PS 1-16 Pwr Save DutyC tE oFF Transmit inhibit to oFF Transmit timeout Lb 4 Freq Lock time Ar oFF Touchtone reply |
| 25-Aug-2005 |  |